## Slide 1: Mzkit User Manual
BioNovoGene Bio-Pharm Technology Co., Ltd
Present: BioDeep R&D Department
E-Mail: R&D@biodeep.cloud
BioNovoGene m/z Data Toolkit User Manual
January, 2021, SuZhou, China

## Slide 2: Introduction
The main function of Mzkit includes:
Raw Data Viewer
Metabolite Feature Annotation
Mulecular Networking
Open Source M/z Raw Data File Format Supports:
mzML, mzXML, imzML, mzPack, netCDF, HDF, Mgf

## Slide 3: LICENSE
Mzkit application and its source code is distributed under the MIT open source license
Source Code:
https://github.com/xieguigang/mzkit
Downloads:
http://www.biodeep.cn/downloads?lang=en-US
This document is distributed under Creative Commons Attribution-ShareAlike 4.0 International Public License

## Slide 4: Screenshots
c. 2D Scatter
d. MS-Imaging
a. Chromatography
b. Spectrum

## Slide 5: Main Screen
The main screen page of Mzkit application.
Data Explorer
Content Viewer
Content Properties
Status Toolstrip
Toolkit Ribbon

## Slide 6: View Untargeted Data

## Slide 7: Introduction
Mzkit supports for view data content in common used open source mzXML and mzML file.
Although the raw data file is in various format, but the mass spectrum data in both of them can be unify into the identical data model for downstream visualization or data analysis in Mzkit.

## Slide 8
Imports Raw Data
Due to the reason of the data size of untargeted metabolomics raw data file is very large, and reading the raw data in text file is usually slowly. So you should always imports the raw data file into Mzkit at first and then you can view the raw data content in Mzkit.
Open Single File
The file open button accepts many file formats, but only supports one file in one click
Imports Multiple Files
Use the context menu on the file explorer for imports a set of raw data files in batch
A progress bar dialog will appear if this is the first file
that imports into mzkit
The imports progress will be running in background is the first file have been
imported into mzkit. You can view the progress in task list tab.

## Slide 9: View 2D Scatter Snapshot
The 2D scatter snapshot of a raw data file is consist with m/z and rt these two dimension data plot. And the scatter color is mapping to the ms1 ion intensity. Just click on the file node on the file explorer then you will see the 2D scatter snapshot of your raw data file.
Select File Node
Just click on the file node to view its 2D scatter snapshot

## Slide 10: View TIC/BPC
Both the TIC and BPC plot is a kind of time-signal plot but with different meanings.
TIC is the chromatography plot of total ions.
BPC is the Chromatography plot of the max intensity ion.
View Chromatography
View TIC/BPC from the contex menu of the file explorer. If multiple file was selected, then TIC/BPC overlaps will be display

## Slide 11: View Scan Feature
The raw data is consists with multiple spectrum scans in MS1 or MS2 levels
The scan in a raw data file is organized in a tree liked data: A parent MS1 scan contains multiple product ion scans.
View Mass Spectrum
Click one of the scan node in the Feature explorer for view its mass spectrum data.

## Slide 12: View XIC
XIC plot is a kind of time-signal plot which is very similar to TIC or BPC.
XIC comes from a set of specific product ion with their parent intensity correlation to scan times.
View XIC Chromatography
Click one of the Ms2 scan node in the Feature explorer, and then select Show XIC on context menu for view its Chromatography plot

## Slide 13: View PDA
PDA plot is a kind of time-signal plot which is very similar to the TIC plot.
Electromagnetic radiation spectrum is supported in mzML file, mzXML file format is not supprted.
Show PDA
Just select the Show PDA menu item on the context menu in the UV scans explorer

## Slide 14: View UV scans
Electromagnetic radiation spectrum is supported in mzML file, mzXML file format is not supprted.
Show UV Overlap
Just select the Show UV Overlap menu item on the context menu in the UV scans explorer. If multiple scan was selected, then UV scan overlap will be plot

## Slide 15: MS-Imaging Viewer

## Slide 16: Introduce MS-Imaging
Mass spectrometry imaging (MSI) is a technique used in mass spectrometry to visualize the spatial distribution of molecules, as biomarkers, metabolites, peptides or proteins by their molecular masses. By choosing a peak in the resulting spectra that corresponds to the compound of interest, the MS data is used to map its distribution across the sample. This results in pictures of the spatially resolved distribution of a compound pixel by pixel.
Römpp A, Spengler B. Mass spectrometry imaging with high resolution in mass and space.
Histochemistry and Cell Biology. 2013 Jun;139(6):759-783.
DOI: 10.1007/s00418-013-1097-6.

## Slide 17: imzML for MS-imaging
Mzkit Supports the imzML file format for view ms-imaging content.
[Main] Open
Select imzML format
Select ion for view image
Steps for view MS-imaging
in Mzkit:

## Slide 18: MS-imaging
MS-imaging in Mzkit
Ion Explorer
Select one ion or multiple ions at here.
Context menu on mouse right click for run image rendering.
Render Options
Tweaks of the MS-Imaging rendering options
Content Viewer
View MS-Imaging rendering image output

## Slide 19: View GC-MS Targeted

## Slide 20: View GC-MS Targeted
The GC-MS targeted data in CDF file format is supported in Mzkit.
View GC-MS targeted data in Mzkit includes view TIC data and SIM ions for metabolite quantification.
[Main] Open
Select CDF format
View GC-MS data in Mzkit
Steps for view GC-MS targeted data
in Mzkit:

## Slide 21: View GC-MS Targeted
View SIM Ions Of GC-MS Targeted
Feature Explorer
Select one ion at here for view mass spectrum plot data.
Select TIC node for view TIC plot of the current GC-MS experiment
Peak Explorer
View Ion peak on TIC at here, and select rt range with mouse drag.
Content Viewer
View the mass spectrum of the selected ion peak

## Slide 22: View LC-MS/MS Targeted

## Slide 23: View LC-MS/MS Targeted
MRM stands for Multiple Reaction Monitoring.
In MRM, a specific ion (precursor ion) is selected in Q1 (first stage MS) from among various ions ionized by the ionization probe, the ion is destructed (collision-induced dissociation) in the collision cell (Q2, collision chamber), and a specific ion is detected from among the destructed ions (product ions) in Q3 (second stage MS).
Multiple channels can be set in one measurement.
[Main] Open
Select mzML format
View LC-MS/MS data in Mzkit
Steps for view LC-MS/MS targeted data
in Mzkit:

## Slide 24: View LC-MS/MS Targeted
View LC-MS/MS Targeted MRM data in Mzkit
Feature Explorer
Select one ion pair at here for view extracted ion chromatography
plot data.
Select TIC node for view TIC plot of the current LC-MS/MS experiment
Content Viewer
View the mass spectrum of the selected ion peak

## Slide 25: 感谢观看
苏州帕诺米克生物医药科技有限公司
Thank you for your attention
地址：江苏省苏州市工业园区新平街388号22幢2层
电话：0512-62959105
邮箱：info@bionovogene.com
网址：https://www.bionovogene.com www.biodeep.cn
科研服务公众号
健康服务公众号
科研服务订阅号